Bryan Berns

ECE 313 – Optics Lab

Lab 5 – Optoelectronic Devices

Data, Calculations, and Graphs:

| ILED | IGE | ISE (nA) |  |
| --- | --- | --- | --- |
| 3.3 | 4.1 | 41.6 |  |
| 8.3 | 5.1 | 115.8 |  |
| 13.3 | 5.4 | 197.3 |  |
| 18.3 | 5.6 | 280.8 |  |
| 23.3 | 5.8 | 336.4 |  |
| 28.3 | 5.8 | 452.0 |  |
| 33.3 | 5.9 | 537.0 |  |
| 38.3 | 5.9 | 618.0 |  |
| ILED | POUT |  |  |
| 3.3 | 98.7 |  |  |
| 8.3 | 3.3 |  |  |
| 13.3 | 5.6 |  |  |
| 18.3 | 2.3 |  |  |
| 23.3 | 8.3 |  |  |
| 28.3 | 9.2 |  |  |
| 33.3 | 10.0 |  |  |
| 38.3 | 10.6 |  |  |
| ILED | VLED | PLED | RESPONSITIVTY |
| 3.3 | 1.4 | 98.7 |  |
| 8.3 | 1.4 | 3.2 |  |
| 13.3 | 1.5 | 5.5 | 0.3 |
| 18.3 | 1.5 | 7.0 | 0.3 |
| 23.3 | 1.6 | 8.2 | 0.3 |
| 28.3 | 1.6 | 9.1 | 0.3 |
| 33.3 | 1.6 | 9.8 | 0.3 |
| 38.3 | 1.7 | 10.5 | 0.3 |
| ILAS | VLAS | PLAS | RESPONSITIVTY |
| 3.3 | 1.5 | 99.0 |  |
| 8.3 | 1.5 | 5.5 |  |
| 13.3 | 1.6 | 9.8 | 1.2 |
| 18.3 | 1.7 | 15.2 | 4.7 |
| 23.3 | 1.7 | 30.3 | 207.7 |
| 28.3 | 1.7 | 33.9 | 276.6 |
| 33.3 | 1.8 | 35.8 | 269.4 |
| 38.3 | 1.8 | 37.1 | 265.3 |

All currents given in mA and voltages in V unless otherwise indicated.

| Material | Dark Current |
| --- | --- |
| Si | .11 nA |
| Ge | 4.10 uA |
| Type | Peak Intesnity Wavelength | Half Power Left | Half Power Right | Full Wave Half Power Spectral Width |
| Laser | 855.3 nm | 839.9 nm | 869.22 nm | 29.32 nm |
| LED | 841.3 nm | 825.3 nm | 860.7 nm | 35.00 nm |

Saturation occurs around 25 mA in both.

Questions:

| Material | Energy Band Gap | Wavelength Maximum |
| --- | --- | --- |
| Si | 1.12 | 1.11 |
| Ge | 0.66 | 1.88 |
| GaAs | 1.42 | 0.87 |
| InP | 1.31 | 0.95 |

- Identify the semiconductors which could be used to make photodiodes for the telecommunications wavelengths of 1.3 um and 1.55 um?

1.3 < 1.88 so Germanium is adequate.

1.55 < 1.88 so Germanium is adequate.

- Why is the Ge detectors responsivity smaller?

Germanium more highly doped with electronics so they are less likely to recombine so an electron is more likely to escape the device, result in more power output.

- Which photodiode produces the larger dark current and why?

Again being more highly doped and having a smaller bandgap, thermal generation is more likely to occur in Germanium thus resulting in dark current.

- Responsivity of Ge at 1.55 um?

Other notes:

The laser spectral width is lower than the LED’s, as expected.