ECE 351

Section 5

Fall 2002

Experiment 3 Pre Lab Report

Submitted by: Bryan Berns

Description of Laboratory Exercise

Create a multiplier that will multiply a three bit input by a constant of 5.

Answers to Assignment Questions

First Set:

a.	Verified on sheet; You can simply sum the outputs of Y0 – Y5, with there correct magnitudes to get the corresponding multiple of 5 to the input X0 – X2 (with it’s corresponding magnitudes).

b.	Verified on sheet; As different values of A/B occur, the buffer is enabled, letter C, D, or E through.

c.	They are the same expect for when A = 1 and B = 1, at which time the multiplexer lets Vcc through (1) and the three state selector will let E through.

d.		Yes

Second Set:

a.	24.115 ns

b.	X0

c.	Y2

d.	Shown On Attached Timing Report

Third Set:

a.	22.4 ns

b.	Very Close 22.4 approximately equal to 22.33

c.	Y0, Y2

Attachments

Café Simulation

Schematic – Multiplier

Schematic – Three State / Multiplexer

Schematic – Disable Logic, Counter

Simulation – Functional

Simulation – Timing

PAD Report

Post Layout Timing File

Partial Timing Simulation, Maximum Delay

Conclusion

Using XILINX, I was successfully able to create, simulate, and analyze a multiplier, multiplexer, counter, three-state selector for time delays and correct logic.

CAFÉ Simulation Output

Connection Arrays from Equations   Oct  5 2002  13:15:56   Page 1

File:  comb.cafe                     Run Options:  x

1:  <table>

2:  3 X2 X1 X0.

3:  6 Y5 Y4 Y3 Y2 Y1 Y0.

4:  000 000000

5:  001 000101

6:  010 001010

7:  011 001111

8:  100 010100

9:  101 011001

10:  110 011110

11:  111 100011.

12:  <process>

13:  e Y5 Y4 Y3 Y2 Y1 Y0.

Y1 = X1

Y0 = X0

Y5 = X2*X1*X0

Y4 = X2*-X1*X0 + X2*-X0

Y3 = -X2*X1 + X2*X1*-X0 + X2*-X1*X0

Y2 = -X2*X0 + X2*-X0

0.010 seconds